Revised 7/25/06

FT-30 PALAZZO URN FOUNTAIN

(FIVE PIECES)

General Fountain Tips – Install fountains on a level surface.  You will need a properly grounded 110-volt (AC only) GFCI protected receptacle near the fountain for your pump.  All pumps are submersible and must be completely underwater to function properly.  Test all pumps and adjust to full output prior to assembly. You should have a tube of clear 100% Silicone caulk to seal the cord exit area.

Place basin, part D on a hard level surface. It is not recommended that fountains be placed directly on grass or dirt.  Determine if part D is level using a level, shim if necessary.  Position the channel opening at the base of Part D toward the electrical outlet to be used since the pump cord will be threaded through this opening

Insert pump into bottom of Part D. Thread cord through the standpipe at the center of Part D.  Then, lift Part D and thread cord through channel opening at the base of Part D.  Gently pull on the cord until all but a little slack remains sufficient to allow the pump to rest easily on the bottom of Part D. Level Part D, shim if necessary.

Place Part C onto the center of Part D using guideline etched into the bottom of Part D with pump in center of Part C. Place Part B onto the opening at the center of Part C. Level Part B, shim if necessary. Attach the long single end of the plastic tube to the pump and each of the four short subsidiary hoses to the four copper pipes inside Part B.  Place Part A squarely on top of Part B. Tilt Part A gently, holding it securely so that it will not slide off of Part B. Attach the remaining end of the black tubing to the copper pipe directly in the center of the bottom of Part A. The remaining off center pipe will function as a drainpipe.  Reposition part A securely on the center of Part B. Level part B, shim if necessary.  Attach two copper pipes to the two pipes protruding from inside the bowl of part A using the copper sleeves provided to make the connection. Attach the plastic spray head to the top of the center outflow pipe.

Fill Parts A and D with water. Plug cord into a GFCI protected receptacle.  Adjust water flow to desired effect using knob adjustor on the pump and/or tubing clamps provided to restrict or redirect water flow.  Adjustment in fountain positioning may be required to control proper water cascade. Insert window, Part CC into the window opening at the base of Part C.

-Winter Care-

Fountain bowls/tops and other fountain components, which collect water, should not be left outside in the winter since any component, which fills with water and freezes may crack. Likewise components such as pedestals, which remain in a basin, filled with water, which then freezes, may also crack or crumble. Ideally, therefore, a fountain should always be stored indoors or in a dry protected place such as a covered porch away from the elements. However, if a fountain must be left outside:

(1) Remove pump, rubber stoppers, drainpipes, finials, and other small components for storage indoors. Note that stoppers or drainpipes are removed to allow drainage in the event water accumulates in any basin.

(2) Raise fountain base from ground with wood strips so that base will not freeze to the ground surface.

(3) Cover or wrap the fountain with burlap or other absorbent material (old blanket or towel) and then cover securely with plastic, making sure that water will not accumulate in the basin or other fountain component and freeze;

(4) Check fountain periodically to insure that plastic is secure and water is not accumulating in any fountain component.

Revised 7/25/06

# Text boxes

FT-30 PALAZZO URN FOUNTAIN

Revised September 18, 2006                                   (5 pieces)

(A)

18”w x 21”h

134 lbs

(B)

12”w x 16.5”h

115 lbs

(C)

12”w x 8”h

52 lbs

(CC)

5”w x 5”h

4 lbs

(D)

45”w x 11”h

579 lbs

# Pump Kit Parts List

Pk700 pump (1)

Approx. 6” length of ¾” clear tubing (1)         		Wedges (4)

approx. 24” length of ½”black non-kink tubing (1)         	#7 Rubber Stopper (1)

approx. 6” length of ½” black non-kink tubing (7)		plastic spray head (1)

large T connector ½”x¾”x ½: (1)     			Hose clamps (6)

½”x½”x½” T connector (3)                                                    Plumber putty

8” length of 3/8” i.d. copper  pipe (2)

3/8” i.d 1/2" o.d copper sleeves (3)

Note – Hose clamps may be used as flow restrictor

Spitter assembly inside column

6” length of Non-kink plastic tubing

# Ft-30 piping system

Bottom of urn assembly

6” lengths of Non-kink tubing to each side spitter

Small “T” connectors

Rubber stopper #7 in bottom of bowl

pump

6” clear plastic tubing

Large “T” connector

24” length of Non-kink plastic tubing

8” copper pipes

1” copper coupling

Sprinkler head

3/8” i.d. 1/2”       o.d. copper coupling