General Fountain Tips – Install fountains on a level surface.  You will need a properly grounded 110-volt (AC only) GFCI protected receptacle near the fountain for your pump.  All pumps are submersible and must be completely underwater to function properly.  Test all pumps and adjust to full output prior to assembly. You should have a tube of clear 100% Silicone caulk to seal the cord exit area.

Place basin (Part E) on a hard level surface. It is not recommended that fountains be placed directly on grass or dirt.  Determine if part E is level using a level, shim if necessary.  Position the channel opening at the base of Part E toward the electrical outlet to be used since the pump cord will be threaded through this opening

Set pump onto bottom of Part E. Tilt Part E to one side and thread cord through the hole and channel opening at the base of Part E.  Gently pull on the cord until all but a little slack remains sufficient to allow the pump to rest easily on the bottom of Part E. Attach the rubber stopper around the cord above the hole in the bottom of Part E and firmly press the stopper into the hole until the top of the stopper is almost level with the top of the hole. Caulk to seal.

Attach short piece of tubing to pump and thread thru part D, center Part D over pump and level. Shim if necessary.  Thread short tubing through part C as you place part C on top of part D, level if necessary. Connect short tubing to pipe in bottom of Part B. Place Part B on top of Part C, level if necessary. Attach long tubing to top of pipe inside part B, attach the other end of the tubing to bottom of Part A, place Part A on top of Part B.

Fill basin part E with water to about an inch below part C.

Plug cord into a GFCI protected receptacle.  Adjust water flow to desired effect.  Adjustment in fountain positioning may be required to control proper water flow.

-Winter Care-

Fountain bowls/tops and other fountain components, which collect water, should not be left outside in the winter since any component, which fills with water and freezes may crack. Likewise components such as pedestals, which remain in a basin, filled with water, which then freezes, may also crack or crumble. Ideally, therefore, a fountain should always be stored indoors or in a dry protected place such as a covered porch away from the elements. However, if a fountain must be left outside:

(1) Remove pump, rubber stoppers, drainpipes, finials, and other small components for storage indoors. Note that stoppers or drainpipes are removed to allow drainage in the event water accumulates in any basin.

(2) Raise fountain base from ground with wood strips so that base will not freeze to the ground surface.

(3) Cover or wrap the fountain with burlap or other absorbent material (old blanket or towel) and then cover securely with plastic, making sure that water will not accumulate in the basin or other fountain component and freeze;

(4) Check fountain periodically to insure that plastic is secure and water is not accumulating in any fountain component.

# Text boxes

Non kink tubing

Pump

Rubber Stopper

(E) 34”W  x 8.5”H

191 lbs

(D) 25”W x 5”H

26 lbs

(C) 77”W x 2.5”H

66 lbs

(B) 12”W x 21”H

49 lbs

- 12.5”W x 5”H

26 lbs

Non-kink tubing

FT-41 Bisbalos Fountain

Revised October 6, 2006			         (5 pieces)

Pump Kit Parts List

PK300 pump (1)						Hose clamps (5)

#7 Rubber stopper (1)					Wedges (4)

Approx. 25” length of ½” Black Non-kink tubing (1) 	Plumber putty

Approx. 12” length of ½” Black Non-kink tubing (1)

Note – Hose clamps may be used as flow restrictor

Non kink tubing