-Winter Care-

Fountain bowls/tops and other fountain components, which collect water, should not be left outside in the winter since any component, which fills with water and freezes may crack. Likewise components such as pedestals, which remain in a basin, filled with water, which then freezes, may also crack or crumble. Ideally, therefore, a fountain should always be stored indoors or in a dry protected place such as a covered porch away from the elements. However, if a fountain must be left outside:

(1) Remove pump, rubber stoppers, drainpipes, finials, and other small components for storage indoors. Note that stoppers or drainpipes are removed to allow drainage in the event water accumulates in any basin.

(2) Raise fountain base from ground with wood strips so that base will not freeze to the ground surface.

(3) Cover or wrap the fountain with burlap or other absorbent material (old blanket or towel) and then cover securely with plastic, making sure that water will not accumulate in the basin or other fountain component and freeze;

(4) Check fountain periodically to insure that plastic is secure and water is not accumulating in any fountain component.

# Text boxes

Ft- 78 Esplanade Two Tier Fountain

Revised July 28, 2006 		(7 pieces)

(A)

5”W x 8.5”H

5 lbs

(B)

15.25”W x 4”H

20 lbs

(C)

7”W x 9.75”H

15 lbs

(D)

28.5”w x 10.75”H

101 lbs

(E)

11”W x 14.25”H

59 lbs

(EE)

5”L x 2”W x 4.5”H

3 lbs

(F)

46.5”W x 9.5”H

432 lbs

Pump Kit Parts List

300 pump

#10 rubber stopper (1)

Approx. 13” length of ½” Black non-kink tubing (1)

Approx. 25” length of ½” Black non-kink tubing (1)

Hose clamps (5) Note – Hose clamps may be used as flow restrictor

Wedges (4)

Plumber putty

Non kink tubing

Non kink tubing

Rubber stopper

pump