Revised September 18, 2006

General Fountain Tips – Install fountains on a level surface.  You will need a properly grounded 110-volt (AC only) GFCI protected receptacle near the fountain for your pump.  All pumps are submersible and must be completely underwater to function properly.  Test all pumps and adjust to full output prior to assembly.  You should have a tube of clear 100% Silicone caulk available to seal area at cord exit.

Place base (part C) on a hard level surface. It is not recommended that fountains be placed directly on grass or dirt.  Determine if part C is level using a level, shim if necessary.  Position the channel opening at the base of Part C toward the electrical outlet to be used since the pump cord will be threaded through this opening

Insert pump into bottom of Part B. Thread the pump cord through the hole at the bottom of part B. Place Part B squarely on top of part C. Tilt Part B to one side and thread cord through the channel opening at the base of Part C.  Gently pull on the cord until some slack (6-8 inches) remains inside Part B.  Attach the rubber stopper around the cord above the hole in the bottom of Part B and firmly press the stopper into the hole until the top of the stopper is almost level with the top of the hole. Caulk to seal.

Attach flexible black tubing to the copper pipe at the bottom of part A.  Place Part A onto Part B so that Part A rests on the 4 interior supports inside Part B. Loop the tubing and attach the other end of the tube to the pump, gently tilting Part A if necessary to allow access to pump. Reposition Part A securely on the 4 interior supports of Part b.

Fill Part B with water. Note that the fountain was not designed so that the basin would not be filled completely with water.  Although filling the basin completely will not affect the operation of the fountain, filling the basin only half way will enhance the sound of the fountain.

Plug cord into a GFCI protected receptacle.  Adjust water flow to desired effect.  Adjustment in fountain positioning may be required to control proper water

cascade.

-Winter Care-

Fountain bowls/tops and other fountain components, which collect water, should not be left outside in the winter since any component, which fills with water and freezes may crack. Likewise components such as pedestals, which remain in a basin, filled with water, which then freezes, may also crack or crumble. Ideally, therefore, a fountain should always be stored indoors or in a dry protected place such as a covered porch away from the elements. However, if a fountain must be left outside:

(1) Remove pump, rubber stoppers, drainpipes, finials, and other small components for storage indoors. Note that stoppers or drainpipes are removed to allow drainage in the event water accumulates in any basin.

(2) Raise fountain base from ground with wood strips so that base will not freeze to the ground surface.

(3) Cover or wrap the fountain with burlap or other absorbent material (old blanket or towel) and then cover securely with plastic, making sure that water will not accumulate in the basin or other fountain component and freeze;

(4) Check fountain periodically to insure that plastic is secure

and water is not accumulating in any fountain component.

# Text boxes

FT-37 BARCELONA FOUNTAIN

(3 pieces)

(A)

10”W x 16”H

90 lbs

(B)

17 ½”W x 12”H

166 lbs

(C)

116”W x 3”H

24 lbs

# Pump Kit Parts List

PK140 Pump

Approx. 23” length of ½” black non-kink tubing (1)

#7 Rubber stopper (1)

Wedges (4)

Hose clamps (3)

Plumber putty

Note – Hose clamps may be used as flow restrictor

Pump

Rubber Stopper

Non Kink Tubing