Revised November 3, 2006

General Fountain Tips – Install fountains on a level surface.  You will need a properly grounded 110-volt (AC only) GFCI protected receptacle near the fountain for your pump.  All pumps are submersible and must be underwater to function properly.  Test all pumps and adjust to full output prior to assembly. You should have a tube of clear 100% Silicone caulk to seal the cord exit area.

Install two hooks on the wall to correspond to the metal loops at the back of the fountain. The hooks should be able to support at least 150 lbs.

Insert pump into bottom of Fountain. Thread the pump cord through the hole inside the basin of the fountain.  Gently pull on the cord until all but a little slack remains sufficient to allow the pump to rest easily on the bottom of the basin. Attach the rubber stopper around the cord at the height of the hole and firmly press the stopper into the hole until the stopper is flush with the hole.

Attach flexible black tubing to the Pump. Attach the other end of the tube to the copper pipe protruding from the inside of the fountain basin. Fill basin with water, being careful not to overfill.

Plug cord into a GFCI protected receptacle.  Adjust water flow to desired effect.  Adjustment in fountain positioning may be required to control proper water

cascade.

-Winter Care-

Fountain bowls/tops and other fountain components, which collect water, should not be left outside in the winter since any component, which fills with water and freezes may crack. Likewise components such as pedestals, which remain in a basin, filled with water, which then freezes, may also crack or crumble. Ideally, therefore, a fountain should always be stored indoors or in a dry protected place such as a covered porch away from the elements. However, if a fountain must be left outside:

(1) Remove pump, rubber stoppers, drainpipes, finials, and other small components for storage indoors. Note that stoppers or drainpipes are removed to allow drainage in the event water accumulates in any basin.

(2) Raise fountain base from ground with wood strips so that base will not freeze to the ground surface.

(3) Cover or wrap the fountain with burlap or other absorbent material (old blanket or towel) and then cover securely with plastic, making sure that water will not accumulate in the basin or other fountain component and freeze;

(4) Check fountain periodically to insure that plastic is secure and water is not accumulating in any fountain component.

# Text boxes

SUSSEX WALL FOUNTAIN

FT-39 (Cast Stone)

94-387-XX01 (Lite)

28”H x 18”W

77 lbs (cast stone)

18 lbs (Lite)

# Pump Kit

Parts List

PK80 pump (1)

Approx 6” length of ½” black non-kink tubing (1)

Rubber stopper # 7 (1)

Hose clamps (3)

Plumbers putty

Note – Hose clamps may be used as flow restrictor

CAST STONE:

position of back hooks:

There are 4 hooks positioned on the back. The two at the top are faced  like upside down letter U, and at 5” from top and 3.75” from sides.

The two at the bottom are placed like letter U but angled toward the corners.

They are positioned  a little differently, the one on the side by the hole(which is on right side of rear view) is positioned at 3.75” from side and 3.25” from bottom, and the other side is positioned 3.25” from side and 3.25” from bottom. Measured from center of U curve. Please note these are best approximation as they are placed in mold by hand as nearly consistent as possible.

Rubber stopper

Non Kink Tubing

Pump